## Slide 1: Driver Station Dashboards Using HTML + Javascript
Dustin Spicuzza
September 10, 2016
NE FIRST University Day

## Slide 2: Agenda
History + Alternatives
Why HTML + Javascript
How it works
Getting started
Real dashboard code
Demos

## Slide 3: Intended Audience
Some familiarity with a browser
Some programming experience
  If you don’t… that’s ok too

## Slide 4: Who Am I?
Software engineer at BBN Technologies
Mentoring FRC since 2009
Co-maintainer of RobotPy since 2010
My team’s UI-related awards:
  2012 Boston Regional; Innovation in Control
  2013 Boston Regional; Innovation in Control
  2014 Virginia Regional; Industrial Design
  2015 Greater DC Regional; Innovation in Control
  2016 Chesapeake Champs; Innovation in Control

## Slide 5: Who Am I?
Software engineer at BBN Technologies
Mentoring FRC since 2009

## Slide 6: Dashboards
Back in the day…
Lots of options now
  LabVIEW Dashboard
  SmartDashboard/SFX
  Custom (Java, C#, et al)

## Slide 7: Dashboard Applications
Robot Control by secondary operator
  Click a button, make something happen
Set up autonomous mode
  Makes it easy to switch between different mode settings on the fly

## Slide 8: Dashboard Applications
Tuning the robot
  Changing positions dynamically
  Better than constant code redeploy!
Providing visual feedback for sensors
  Good for debugging hardware issues

## Slide 9: My JOURNEY
Dashboards

## Slide 10: My Journey: 2009/2010
WebDMA (C++)

## Slide 11: My Journey: 2009/2010
WebDMA (C++)
Not actually a dashboard
Ran an in-process webserver on the cRIO
  UI was HTML/JS
Great for tuning

## Slide 12: My Journey: 2012
Show ball when sensor is on
But…
Little/poor documentation
Java swing is complicated
Layout is terrible
Hard to setup
Custom SmartDashboard widget (Java)

## Slide 13: My Journey: 2013/2014
PyGTK + touchscreen laptop

## Slide 14: My Journey: 2013/2014
PyGTK + touchscreen laptop
Very shiny
Integrated with image processing
Communications via pynetworktables
But…
Python is great, GTK is not
Difficult to customize interface
Very difficult to teach

## Slide 15: pynetworktables2js
Introducing

## Slide 16: My Journey: 2015 - Present
2015 UI (Team 1418)

## Slide 17: My Journey: 2015 - Present
2016 UI (Team 1418)

## Slide 18: My Journey: 2015 - Present
2016 UI (Team 2423)

## Slide 19: My Journey: 2015 - Present
Interactive camera threshold tuning

## Slide 20: Why pynetworktables2js
TL;DR: It’s simpler
pynetworktables2js lowers the barrier of entry for teams that want an additional way to tune/control their robot with a minimal amount of programming.

## Slide 21: Why pynetworktables2js
TL;DR: It’s simpler
It’s as easy as making a webpage.

## Slide 22: Why pynetworktables2js
Many students already know how to create webpages
  And if not, there’s TONS of ways to learn on the web
Outreach to nontraditional students
  Introduce students to programming concepts
  Artistic students
Yet another way to learn real world skills

## Slide 23: Why pynetworktables2js
Very flexible
  Anything you can do in a webpage
Simple to get started
Cross platform
  Windows + OSX + Linux
Actually has documentation
  Unlike most other dashboard alternatives

## Slide 24: HOW IT WORKS
Let’s get started

## Slide 25: How it works
Browser talks to Python server running on your laptop
Python server uses NetworkTables to communicate with Robot
  Results are passed back/forth to webpage

## Slide 26: How it works
Robot
Code
Webpage
PythonWeb
Server
Websocket
NT
NT
NT
NetworkTables

## Slide 27: How it works
Note that the webserver runs on the laptop
You could run it on the robot
  I don’t recommend this because of bandwidth reasons
  Also, it means you can’t load the page until the robot connects to FMS

## Slide 28: NetworkTables
Easy to use distributed key-value protocol created by WPILib team
Very little setup required*
Latency is “good enough” for 99% of teams
  pynetworktables is 50ms max
* mDNS issues in 2016, hopefully they’ll be fixed in 2017…

## Slide 29: NetworkTables Basics
On the server…
On the client…
table.putString(“key”, “something”)
x = table.getString(‘key’)
// output is ‘something’
printf(“%s\n”, x);

## Slide 30: pynetworktables2js Basics
Very similar to other languages
  getValue/putValue only
  Doesn’t need getNumber/getString/etc
  Uses full path of keys, no tables
// getValue will return the correct type
var coolThing = NetworkTables.getValue(“/table/key”); // putValue doesn’t care about what type you pass NetworkTables.putValue(“/table/string_key”, “my value”);
NetworkTables.putValue(“/table/bool_key”, true);
NetworkTables.putValue(“/table/number_key”, 42.0);

## Slide 31: GETTING STARTED
Let’s get started

## Slide 32: Getting Started
Install pynetworktables2js
  See the documentation
Create a directory with web content
Run the server from inside the directory
Point your browser at http://localhost:8888
On Windows:
py -m pynetworktables2js
On Linux/OSX:
python -m pynetworktables2js

## Slide 33: Your first webpage
<!DOCTYPE html> <html lang=”en”><body>
Connected: <span id=”connected”>false</span>
<!-- Include the API -->
<script src=”/networktables/networktables.js”></script>
<script type=”text/javascript”>
function onConnected(connected) {
document.getElementById(“connected”).textContent = connected;
}
NetworkTables.addRobotConnectionListener(onConnected, true);
</script>
</body>
</html>

## Slide 34: pynetworktables2js API
NetworkTables.addRobotConnectionListener(f)
Calls a function to tell you that the page is connected to the robot
  Driver wants to know if the dashboard isn’t going to actually do anything!

## Slide 35: pynetworktables2js API
NetworkTables.putValue(k,v)
Sets the value in NetworkTables
  Give it ~50ms to get to the Robot
If not connected to robot, value may be discarded

## Slide 36: pynetworktables2js API
NetworkTables.getValue(k, [default])
Returns the current value of a key or null
I rarely use getValue
  What happens if the value changes?
  How do you find out about the change?
If not connected to robot, value isn’t always meaningful

## Slide 37: pynetworktables2js API
NetworkTables.addKeyListener(k, f, [imm])
Set a function that will be called whenever the value for a particular key is changed.
  It will usually call you when the robot connects, as the values will change
  If you set the third parameter to true, it will call you immediately with the current value

## Slide 38: REAL DASHBOARD CODE
Putting it all together

## Slide 39: Putting it all together
Let’s show how to display simple feedback of a digital input
Here’s the steps
  Create an SVG circle element
  Add a listener for the value being sent over NetworkTables
  Change color when the value is received

## Slide 40: Putting it all together
Include the API in your page
<!DOCTYPE html> <html>
<head>
<script src=“/networktables/networktables.js”></script>
</head>

## Slide 41: Putting it all together
Create an SVG circle element
<svg width="100" height="100">
<circle id="switch" cx="50" cy="50" r="40"
stroke="black" stroke-width="4"
fill="gray" />
</svg>

## Slide 42: Putting it all together
<script type=“text/javascript”>
function onSwitchChanged(key, value, isNew) {
// TODO
}
NetworkTables.addKeyListener('/SmartDashboard/switch',
onSwitchChanged, true);
</script>
Add a listener for the value being sent over NetworkTables

## Slide 43: Putting it all together
Change color upon new value
  Hint: Use jQuery to make it easier :)
function onSwitchChanged(key, value, isNew) {
if (value) {
$("#switch").css("fill", "red");
} else {
$("#switch").css("fill", "green");
}
}

## Slide 44: Demo
Putting it all together

## Slide 45: 2015 UI Demo
Putting it all together

## Slide 46: pynetworktables2js API
There’s lots more...
  Read the documentation

## Slide 47: pynetworktables2js API
Useful helper functions for common UI tasks
  Easy toggle button
  HTTP Camera support
  Robot connection indicator
  SendableChooser related helpers

## Slide 48: pynetworktables2js tips
Tell your team to buy a touchscreen laptop
  Very inexpensive these days (<$700)
Create multiple pages, and show them using browser tabs
  One page for teleop
  One page for autonomous options
  One page for tuning

## Slide 49: Future work
pynetworktables2js is a good start…
  Need more widgets/helpers
  Single executable deploy for 2017
  Would love more contributors (hint, hint)
Need a ‘TableViewer’ integrated into pynetworktables2js
  There’s a PR on github, needs work

## Slide 50: Future work
NetworkTables 3.0 support for 2017
  Enables persistent settings
  Can talk to LabVIEW
  Will probably happen…

## Slide 51: Want More?
This presentation + code available online*
  https://github.com/virtuald/frc-dashboard-workshop
* Sometime on Sunday

## Slide 52: FRCDashboard Project
Created by Erik Boesen, student on 1418
Uses Electron framework to run HTML/JS app
  Same thing that Atom text editor uses
Goal is to provide easy customization and expansion using prebuilt modules
Project is still very new

## Slide 53: Resources
pynetworktables2js
  Code + Examples: https://github.com/robotpy/pynetworktables2js
  Documentation: http://pynetworktables2js.readthedocs.io

## Slide 54: Resources
1418’s UI repos
  https://github.com/frc1418/2015-ui
  https://github.com/frc1418/2016-ui
FRCDashboard
  http://frcdashboard.github.io/

## Slide 55: One more thing…
Publicly editable repository of information related to FIRST Robotics
  Technical topics
  Non-technical
  Team pages
Add content to your team’s page!
https://firstwiki.github.io

## Slide 56: Questions
???